## Slide 1: FEBio Workshop
Interactive Tutorial

## Slide 2: Step 1 – setting up geometry
Create new model
Set units to SI
lower arm: create box
  Width = 0.5 m
  Height = depth = 0.05
  Transform to: 0, 0, 0
Upper arm: clone lower arm
  Transform: position = -0.275, 0.275, 0; rotation Z = 90
Muscle: create cylinder
  Radius = 0.05m, height = 0.4m
  Transform: position = -0.15, 0.225, 0; rotate (X= -89.4392, Y = -11.7749, Z = 11.7749)
Weight: create sphere
  Radius = 0.1
  Transform: 0.35, 0, 0
upper arm
lower arm
muscle
weight

## Slide 3: Step 2 – Materials
Create muscle material: trans-iso Mooney-Rivlin
  Bulk modulus (K) = 5e6 Pa
  C1 = 5e4 Pa
  C3 = 50
  C4 = 50
  C5 = 1
  Lam_max = 10 ( essentially ignores the linear region)
  Fiber: vector {-0.2588,0.9659,0}
(Demo Material Test)

## Slide 4: Step 2 - Materials
Create 3 rigid bodies for the 3 other parts
Override COM and set COM to:
  Upper arm: {-0.275,0.275,0.025}
  Lower arm: {-0.275,0,0}
  Weight: {0.35,0,0}

## Slide 5: Step 3 - Mesh
Upper arm: Nx = Ny = Nz = 1
Lower arm: Nx = Ny = Nz = 1
Muscle: (default values)
Weight: segments = divisions = 1
Use ‘m’ shortcut to toggle mesh lines

## Slide 6: Step 4 - Constraints
Add Nodal BC: rigid to bottom and top surfaces of muscle
  Top surface  upper arm
  Bottom surface  lower arm
Add rigid fixed constraints:
  Upper arm: fixed in all dofs
  Lower arm: fixed in X,Y,Z - displacement, X,Y – rotation
  Weight: fixed in z-displacement, X,Y-rotation
Add rigid load to weight:
  Dof: Ry
  Value: -100 N (Notice parameter is load controlled)

## Slide 7: Step 4 - constraints
Add rigid lock to connect lower arm and weight:
  Body_a: lower arm
  Body_b: weight
  Force penalty = moment penalty = 10,000
  Joint origin = {0.25, 0, 0}
  First axis = {1,0,0}
  Second axis = {0,1,0}
  Auto-penalty = on

## Slide 8: Step 5 – Analysis settings
Add an analysis step (name “passive”, default settings)
Make sure to save the file!
Run the model
Open the results file

## Slide 9: Step 6 – active contraction
Add a second step (“active”)
Add “active contraction” to muscle material
  Ascl = 1 (add linear load curve (1,0)  (2,1))
  Tmax = 1e5
  Ca0= camax = 4.35
  Beta = 4.75
  L0 = 1.58
  refL = 2.04
Rerun model again

## Slide 10: Step 7 - Optimization
FEBio  Generate optimization file
  Add parameter: fem.material('muscle').c1 : 1e4, 5e3,1e5
  Add parameter: fem.material('muscle').c3 : 30, 10, 100
  Objective: fem.rigidbody('weight').position.y
  Data:
Save optimization file (e.g. sb3c_opt.feb)
Run optimization problem:
  Advanced  task name = optimize, control file = sb3c_opt.feb
  Solution: c1 = 50000, c3 = 50
0 0
0.1 -0.01956
0.2 -0.03925
0.3 -0.05873
0.4 -0.07729
0.5 -0.09405
0.6 -0.10852
0.7 -0.12078
0.8 -0.13116
0.9 -0.14006
1 -0.1478